## Slide 1
Antenna Summit

## Slide 2: Introduction
Instructor : Bill Smith, KQ1S
  Amateur Extra
  Licensed since 1983
The ARRL Handbook for Radio Communications, 98th Edition, 2021
Q & A at end of session

## Slide 3: Course Overview
        Mathematics Review
        Electricity, Power, and Energy
        Basic Circuit Principles
        Resistance, Conductance, Capacitance, and Inductance
        Kirchhoff’s Laws
        Thevenin’s and Norton’s Theorems
        Power and Energy

## Slide 4: Easy Math Review
Order of mathematics operations - Remember BODMAS
  Work within Brackets first
  (Order of the operations is important)
  Perform Divisions and Multiplications as you encounter them – Inside of brackets first, then outside
  Perform Additions and Subtractions as you encounter them – Inside of brackets first, then outside
  Let’s look at a few examples…

## Slide 5: Easy Math Review
Remember - BODMAS
  Ex. 1 10 – 2 x 3
    = 10 – 6
    = 4
  Ex. 2 (10 – 2) x 3
    = 8 x 3
    = 24

## Slide 6: Easy Math Review
Remember – BODMAS
  Ex. 3 -4 + 5 x (7 + 3)
    = -4 + 5 x 10
    = -4 + 50
    = 46

## Slide 7: Easy Math Review
Remember – BODMAS
  Ex. 4 12 (5 + 6 x 3) / (4 + 2)
    = 12 (5 + 18) / 6
    = 12 x 23 / 6
    = 276 / 6
    = 46

## Slide 8: Easy Math Review
Remember – BODMAS
  Ex. 5 -2 (x + 5 x 7 + 3)
  = -2 (x + 35 + 3)
  = -2 (x + 38)
  = -2x - 76

## Slide 9: Additional Math Resources
Chapter 2 Downloadable Supplemental Material
  “Radio Mathematics”
  “Radio Math Formulas and Notes”
  “Scientific and Engineering Notation”
  “Understanding a Scientific Calculator”

## Slide 10: Electrical Fundamentals
Atoms and Molecules
  Atom – Primary building block of all matter
  Construction – Nucleus (Protons, Electrons, Neutrons)
    Protons – Positively (+) charged
    Electrons – Negatively (-) charged
    Neutrons – No charge
  Molecule – Two or more atoms bonded together

## Slide 11: Electrical Fundamentals
Atoms and Molecules
  Electrically Neutral – Atoms and Molecules carry no charge until acted upon a chemical, mechanical, or electrical process
  Positively (+) Charged Atom or Molecule = More protons than electrons
  Negatively (-) Charged Atom or Molecule = More electrons than protons
  Ions – Charged atoms or molecules
    Free Electrons – (Not bound to an atom) because they are negatively (-) charged

## Slide 12: Electrical Fundamentals
Electrical Charge, Voltage, and Current
  Current – Movement of electrical charge between poles of voltage source
  Current Flow Conventions
    Electron Current – Negative charges (electrons) move from the negative voltage pole to the positive voltage pole

## Slide 13: Electrical Fundamentals
Electrical Charge, Voltage, and Current
  Current Flow Conventions
    Conventional Current – Positive charges move from the positive voltage pole to the negative voltage pole – Used throughout “The ARRL Handbook”

## Slide 14: Electrical Fundamentals
Units of Measurement
  Volt (V) – The difference in electrical protentional between two points
  Ampere (A) – Amount of current flow between voltages
  Coulomb (C) – Electrical charge = 6.25 x 1018 electrons or protons

## Slide 15: Electrical Fundamentals
Types of Current
  Direct Current (DC) – Electrical current allowed by the voltage source to flow in only one direction (e.g., A battery with positive and negative poles)
    Steady State DC – Current is positive relative to zero and does not vary
    Pulsating DC – Current is always positive relative to zero, regardless of variation
    Intermittent DC – Current is positive but periodically reaches zero

## Slide 16: Electrical Fundamentals
Types of Current
Alternating Current (AC) – Electrical current allowed by the voltage source to flow alternating in both directions (e.g., Regular household current)

## Slide 17: Electrical Fundamentals
Resistance and Conductance
  Conductor – Material in which electrons or ions can move (flow) easily
  Insulator – Material within which electrons or ions have difficulty moving
  Resistance – Essentially the difficulty that moving charges encounter when flowing in a conductor
  Resistor – A component made of material exhibiting a certain amount of resistance
  Ohms () – The amount of resistance to current flow

## Slide 18: Electrical Fundamentals
Resistance and Conductance
  Conductance (G) – The reciprocal of resistance (1/R)
  Siemens (S) – The modern unit of measure of conductance
    Siemens has replaced the obsolete unit Mho
    A resistance of 1 Ohm = conductance of 1 Siemens (1/1)
    A resistance of 1,000 Ohms = conductance of 0.001 Siemens (1/1,000)

## Slide 19: Electrical Fundamentals
Resistance and Conductance
  The amount of current that may flow in a conductor when a certain voltage is applied varies with the resistance of the conductor (Resistivity)
  1 Ohm ( = Amount of resistance that allows 1 Ampere of current to flow between points having a potential difference
  Standard of Resistivity – Conductors are compared to annealed copper
    (See Table 2.1 – Annealed copper = 1.00)

## Slide 20: Electrical Fundamentals
Resistance and Conductance
  Ohm’s Law
    R = E / I
    where
      R = Resistance in ohms
      E = Voltage (or EMF) in volts
      I = Current in amperes
    E = I x R
    I = E / R

## Slide 21: Electrical Fundamentals
Resistance and Conductance
Let’s do a few calculations using the following simple circuit:

## Slide 22: Electrical Fundamentals
Resistance and Conductance
  When E = 150 volts and I = 2.5 amperes, what does R equal?
    R = E / I
    R = 150 / 2.5
    R = 60 Ohms
  When E = 250 volts and R = 5,000 ohms, what does I equal?
    I = E / R
    I = 250 / 5000
    I = 0.050 Amperes or 50 mA

## Slide 23: Electrical Fundamentals
Resistance and Conductance
  When I = 5 amperes and R = 250 ohms, what does E equal?
    E = I x R
    E = 5 x 250
    E = 1250 Volts

## Slide 24: Electrical Fundamentals
Basic Circuit Principles
  Nodes – Any point in a circuit at which current can divide between paths
  Loops – A series of branches making a complete current path from the voltage source back to the opposite side of the voltage source
  Branches – Any unique conducting path between nodes

## Slide 25: Electrical Fundamentals
Basic Circuit Principles

## Slide 26: Electrical Fundamentals
Basic Circuit Principles
Resistors in Parallel
  Resistors in parallel can be represented as a single equivalent resistance
  The equivalent resistance will be a value less than the lowest resistor value
  If all parallel resistors have the same value, divide the resistor value by number of resistors to find parallel resistance value
    Example: five 25 k resistors in parallel = 25 k / 5 = 5 k

## Slide 27: Electrical Fundamentals
Basic Circuit Principles
Resistors in Parallel
The formula for finding equivalent resistance, sometimes referred to as the Reciprocal of Reciprocals formula:

## Slide 28: Electrical Fundamentals
Basic Circuit Principles
Resistors in Parallel
Example: Given three resistors in parallel (5.0 k + 20.0 k + 8.0 k – What is Requiv?

## Slide 29: Electrical Fundamentals
Basic Circuit Principles
Resistors in Parallel
If only two resistors in parallel, then the following formula can be used. (This can also be used to combine parallel resistors two at a time to keep from having to do the Reciprocal of Reciprocals formula)

## Slide 30: Electrical Fundamentals
Basic Circuit Principles
  Kirchhoff’s Current Law – The sum of all currents flowing into a node and all currents flowing out of a node is equal to zero.
  For resistors in parallel
  Expressed Mathematically
    (Iin1 + Iin2 + …) – (Iout1 + Iout2 + …) = 0
    or
    (Iin1 + Iin2 + …) = (Iout1 + Iout2 + …)

## Slide 31: Electrical Fundamentals
Basic Circuit Principles
Kirchhoff’s Current Law Example
Calculate current flow through each resistor (Ix) and circuit current total (ITotal)
E = 250 Volts
R1 = 5.0 k; I1 = E/R1 = 250/5.0k = 50.0 mA
R2 = 20.0 k; I2 = E/R2 = 250/20.0k = 12.5 mA
R3 = 8.0 k; I3 = E/R3 = 250/8.0k = 31.2 mA
ITotal = 50.0 mA + 12.5 mA + 31.2 mA = 93.7 mA
Iin (93.7 mA) – Iout (93.7 mA) = 0

## Slide 32: Electrical Fundamentals
Basic Circuit Principles
Resistors in Series
  Resistors in series can be represented as a single equivalent resistance
  The equivalent resistance will be the sum of the individual resistors
    Requiv = R1 + R2 + R3 + …
    Example: Requiv = 5.0 k + 20.0 k + 8.0 k = 33 k

## Slide 33: Electrical Fundamentals
Basic Circuit Principles
  Kirchhoff’s Voltage Law – The sum of all voltages around a closed current loop is zero.
  Used for resistors in series
  Expressed Mathematically
    E1 + E2 + E3 + ... = 0
    or
    (Esource1 + Esource2 + …) = (Esink1 + Esink2 + …)

## Slide 34: Electrical Fundamentals
Basic Circuit Principles
Kirchhoff’s Voltage Law Example
1. Solve for current (I)
VBatt = 250 Volts; R1 = 5.0 k; R2 = 20.0 k; R3 = 8.0 k
VDrop = -250 + (I x R1) + (I x R2) + (I x R3) = 0
= -250 + I(33 k) = 0
I = -250 + I(R1 + R2 + R3)
= 250/33 k = 0.00758 A or 7.58 mA

## Slide 35: Electrical Fundamentals
Basic Circuit Principles
Kirchhoff’s Voltage Law Example
2. Solve for individual voltage drops
V1 = I x R1 = 7.58 mA x 5.0 k = 37.9 Volts
V2 = I x R2 = 7.58 mA x 20.0 k = 151.6 Volts
V3 = I x R3 = 7.58 mA x 8.0 k = 60.6 Volts
VTotal = V1 + V2 + V3
VTotal = 37.9 Volts + 151.6 Volts + 60.6 Volts = 250 Volts

## Slide 36: Electrical Fundamentals
Basic Circuit Principles
Resistors in Series-Parallel
1. Create an equivalent resistance for R2 & R3 and calculate REQ
= (R2 x R3) / (R2 + R3)
= (20 k x 8 k) / (20 k _ 8 k)
= 1.6 x108 k / 28 k
= 5.714 k
Add R1 & REQ together as series resistors to calculate Rtotal
= 5 k + 5.714 k
= 10.714 k

## Slide 37: Electrical Fundamentals
Basic Circuit Principles
Conductances in Series
  Conductance (G) is the reciprocal of resistance, G = 1/R
  Therefore, conductances is series are calculated like resistors in parallel

## Slide 38: Electrical Fundamentals
Basic Circuit Principles
Conductances in Series
If only two conductances in series, then the following formula can be used. (This can also be used to combine parallel conductances two at a time to keep from having to do the Reciprocal of Reciprocals formula)

## Slide 39: Electrical Fundamentals
Basic Circuit Principles
Conductances in Parallel
  Conductance (G) is the reciprocal of resistance, G = 1/R
  Therefore, conductances is parallel are calculated like resistors in series

## Slide 40: Electrical Fundamentals
Basic Circuit Principles
Thevenin’s Theorem
  Introducing the term network, the formal name for a circuit
  Thevenin’s Theorem – “Any two-terminal network made up of resistors and voltage or current sources can be replaced by an equivalent network made up of a single voltage source and a series resistor”

## Slide 41: Electrical Fundamentals
Basic Circuit Principles
Thevenin’s Theorem
Step 1: Isolate R3 by redrawing the circuit such that R1 and R2 form a voltage divider, with R3 as the load. (The current across R3 is the voltage across R3 divided by its resistance) - (IR3 = VR3 / R3)
Note: that the R2 influences the voltage across R3 and vice versa. The two need to be separated by some mechanism to solve for I.
Example: What is the current (I) through R3?

## Slide 42: Electrical Fundamentals
Basic Circuit Principles
Thevenin’s Theorem
Step 2: Construct a Thevenin Equivalent Circuit to replace everything connected to A and B with a single voltage source and a series resistor
Step 3: Calculate the total circuit current through the network.
The total current (I) in the circuit is calculated:
I = E / (R1 + R2)
= 250 V / (5 k + 20 k
= 250 V / 25 k = 0.010 A or 10 mA

## Slide 43: Electrical Fundamentals
Basic Circuit Principles
Thevenin’s Theorem
Step 4: Calculate the open circuit voltage across A and B with no load
Simply apply Ohm’s Law:
a. Remember that I = E / (R1 + R2)
b. Substitute EAB for I:
I = E/(R1 + R2) and EAB = I x R2,
so EAB = E x R2 / (R1 + R2)
c. Now, calculate open circuit voltage across A&B (EAB):
EAB = 250 V x 20 k/ (5 k + 20 k
EAB = 5 x 106 / 25 k = 200 V
This is known as the Thevenin Equivalent Voltage (EThev)

## Slide 44: Electrical Fundamentals
Basic Circuit Principles
Thevenin’s Theorem
Step 5: Calculate the Thevenin Equivalent Resistor (RThev)
RThev = (R1 x R2) / (R1 = R2)
= (5 k x 20 k) / (5 k + 20 k)
= 1.0 x 108 / 25 k
= 4000 or 4 k

## Slide 45: Electrical Fundamentals
Basic Circuit Principles
Thevenin’s Theorem
Step 6: Calculate the current through the load R3:
IR3 = EThev / (RTotal)
*Note: Rtotal = (RThev + R3)
= 200 V / 4 k + 8 k
= 200 V / 12 k
= 0.0167 A or 16.7 mA

## Slide 46: Electrical Fundamentals
Basic Circuit Principles
Norton’s Theorem
  Norton’s Theorem – “Any two-terminal network made up of resistors and voltage or current sources can be replaced by an equivalent network made up of a single current source and a parallel resistor”
  Very similar to Thevenin’s Theorem, but for current sources rather than voltage sources

## Slide 47: Electrical Fundamentals
Basic Circuit Principles
Norton’s Theorem
Step 1: Isolate RThev by replacing the load resistor R3 with a short circuit.
Step 2: Calculate the current (INorton) through RThev:
Inorton = E / RThev
= 250 V / 5 k = 0.050 A or 50 mA
Example: What is the current (I) through R3?

## Slide 48: Electrical Fundamentals
Basic Circuit Principles
Norton’s Theorem
Step 3: Reinsert the load resistor R3 across A and B.
Step 4: Calculate the circuit current (I) through R3:
- R3 is 2/3 the resistance of RThev
- R3 will therefore have 1/3 the current through it
Step 5: Calculate IR3
Recall that INorton was calculated in Step 2 to be 50 mA
- What is 1/3 of 50 mA?
50 mA / 3 = 16.7 mA
Therefore, the current (I) through R3 = 16.7 mA

## Slide 49: Electrical Fundamentals
Basic Circuit Principles
Thevenin’s & Norton’s Theorems
Final Thoughts
  Thevenin- and Norton-equivalent circuits can be transformed back and forth
  The equivalent resistor is the same in both cases
  The Thevenin equivalent voltage source value is the same voltage as the drop across a Norton-equivalent resistor
  The Norton equivalent current source value is equal to the short circuit current provided by the Thevenin source

## Slide 50: Electrical Fundamentals
Power and Energy
  Power – Measure of the rate at which energy is generated or used
  One watt (W) of power is defined as the generation or use of one joule (J) of energy or work per second
  One joule (J) is the amount of energy or work done when a force of one newton is applied to an object that is moved one meter in the direction of the force

## Slide 51: Electrical Fundamentals
Power and Energy
    One watt (W) is also defined as one volt (V) of electromotive force (EMF) causing one ampere (I) of current to flow through a resistance (*Discussion applies to DC circuits only):
      P = I x E
      P = Power in watts
      I = Current in amperes
      E = EMF in volts

## Slide 52: Electrical Fundamentals
Power and Energy
Power
    Power may also be expressed as horsepower (hp)
      746W = 1 horsepower
    Assumes lossless (100% efficiency) conversion between mechanical and electrical power
    Especially useful measure of work when dealing with motors

## Slide 53: Electrical Fundamentals
Power and Energy
Energy
    Energy is an expression of work
    Energy is generally measured as watt-hours (Wh), which is power multiplied by time:
      Wh = P x t
      Wh = Energy in watt-hours
      P = Power in watts
      t = Time in hours

## Slide 54: Electrical Fundamentals
Power and Energy
Energy
    Power companies bills in kilowatt-hours (kWh)
    Batteries generally are rated in milliampere-hours (mAh)
    Note that a small amount of power used over a long has the same effect as a large amount of power used over a short time

## Slide 55: Electrical Fundamentals
Power and Energy
Energy
  Practical application for Ham Radio:
    A handheld radio has a fully charged battery storing 900 mAh of energy, and the radio draws 30 mA on receive. How long will the radio continue to stay on in receive mode?
    t = 900 mAh / 30 mA
    = 900 mAh / 30 mA
    = 30 hours (*Assuming 100% efficiency)

## Slide 56: Electrical Fundamentals
Power and Energy
Efficiency
  No circuit is 100% lossless
  Every circuit experiences losses as heat or other form of energy
    Law of Conservation of Energy – Energy can neither be created nor destroyed, only converted from one form to another.
  Energy lost to conversion to another form is a loss of efficiency

## Slide 57: Electrical Fundamentals
Power and Energy
Efficiency
  Power converted to heat is considered a loss because it is not useful power
  The ratio of power output to power input results in a measure of efficiency (Eff) usually expressed as a percentage
    Expressed mathematically:
      Eff = Po / Pi
      Eff = Efficiency as a value or fraction between 0 and 1
      Po = Power output in watts (W)
      Pi = Power input in watts (W)

## Slide 58: Electrical Fundamentals
Voltage, Current, Resistance, & Power Equation Summary

## Slide 59: Electrical Fundamentals
Capacitance and Capacitors
Electrostatic Fields and Energy
  Electrostatic Field – Created whenever a voltage exists between two points
    The field causes electrical charges to feel a force in the direction of the field
      If the charges are not free to move, then it is potential energy
      If the charges are free to move, then it is kinetic energy
  The field is represented by lines of force showing the
  direction of the force
  The field’s strength is measured in volts per meter (V/m)

## Slide 60: Electrical Fundamentals
Capacitance and Capacitors
Capacitor – A device with the property of storing electrical energy in an electrical field
Capacitance – The amount of electrical energy that a capacitor can store

## Slide 61: Electrical Fundamentals
Capacitance and Capacitors
The Capacitor
Two flat metal plates placed close to each other without touching and connected to a battery through a switch
The switch (S) is closed, electrons are attracted from upper plate to (+) terminal of battery
3. The same number of electrons are repelled from the (-) terminal and pushed to the lower plate

## Slide 62: Electrical Fundamentals
Capacitance and Capacitors
The Capacitor
Creates an imbalance between the plates resulting in a voltage appearing
Eventually the plates reach equilibrium opposing further current flow
6. At this point, electrical energy is being stored between the plates

## Slide 63: Electrical Fundamentals
Capacitance and Capacitors
  The amount of electrical charge (potential energy) that a capacitor can hold is proportional to the voltage applied and its capacitance:
      Q = C x V
      where
      Q = Charge in coulombs
      C = Capacitance if farads (F)
      V = Electrical potential in volts

## Slide 64: Electrical Fundamentals
Capacitance and Capacitors
  The amount of electrical energy (ability to do work) that a capacitor can store is similarly calculated:
      W = V2C / 2
      where
      W = Energy in joules (J) or watt-seconds
      C = Capacitance if farads (F)
      V = Electrical potential in volts

## Slide 65: Electrical Fundamentals
Capacitance and Capacitors
  Farad – The basic unit of measure of the ability to store electrical energy in an electrostatic field (capacitance)
    Three common measures of capacitors:
      microfarad (10-6 F) – one millionth of a farad
      nanofarad (10-9 F) – one thousandth of a microfarad (one billionth of a farad)
      picofarad (10-12 F) – one millionth of a microfarad (one trillionth of a farad)

## Slide 66: Electrical Fundamentals
Capacitance and Capacitors
Capacitors in Parallel
  Total capacitance of capacitors in parallel is calculated similarly to resistors in series – The total capacitance is equal to the sum of the individual capacitors
    Ctotal = C1 + C2 + C3 + …
    Example: Ctotal = 1.0 uF + 2.0 uF + 4.0 uF = 7 uF

## Slide 67: Electrical Fundamentals
Capacitance and Capacitors
Capacitors in Series
  Total capacitance of capacitors in series is calculated similarly to resistors in parallel – Apply the reciprocal of reciprocals formula

## Slide 68: Electrical Fundamentals
Capacitance and Capacitors
Capacitors in Series
    Example: What is the total capacitance of three capacitors in series when C1 = 1.0 uF, C2 = 2.0 uF, and C3 = 4.0 uF, and the voltage across each capacitor?
          Step 1. Calculate total circuit capacitance:
      Ctotal = 1 / ((1 / 1.0 uF) + (1 / 2.0 uF) + (1 / 4.0 uF))
        = 1 / ((1) + (0.5) + (0.25))
        = 1 / 1.75
        = 0.571 uF

## Slide 69: Electrical Fundamentals
Capacitance and Capacitors
Capacitors in Series
Step 2. Calculate the voltage across each capacitor?
The voltage across each capacitor is proportional to the total capacitance divided by the capacitance of the capacitor in question (E = Ctotal / Cx):
E1 = (0.5714 uF / 1 uF) x 2000 V = 0.5714 x 2000 = 1143 V
E2 = (0.5714 uF / 2 uF) x 2000 V = 0.2857 x 2000 = 571 V
E3 = (0.5714 uF / 4 uF) x 2000 V = 0.1429 x 2000 = 286 V
ETotal = 1143 V + 571 V + 286 V = 2000 V

## Slide 70: Electrical Fundamentals
Basic Circuit Principles
Capacitors in Series
If only two capacitors in series, then the following formula can be used. (This can also be used to combine series capacitors two at a time to keep from having to do the Reciprocal of Reciprocals formula)

## Slide 71: Electrical Fundamentals
Capacitance and Capacitors
Notes for Calculations
  When two or more capacitors are connected in series, the total capacitance is less than that of the smallest capacitor in the group
  When capacitors are connected in series, the applied voltage is divided between them according to Kirchhoff’s Voltage Law
  The voltage rating of capacitors connected in parallel is the lowest voltage rating of any of the capacitors
  When doing calculations, the same units must be used throughout

## Slide 72: Electrical Fundamentals
Capacitance and Capacitors
Charging and Discharging
When voltage is applied across the capacitor, current flows and the capacitor is charged.
Full charge is reached very quickly
Current discontinues when fully charged (*DC)

## Slide 73: Electrical Fundamentals
Capacitance and Capacitors
Charging and Discharging
When voltage is removed or capacitor is shorted, current flows and the capacitor is discharged.
Zero charge is reached very quickly
Current discontinues when fully discharged (*DC)

## Slide 74: Electrical Fundamentals
Capacitance and Capacitors
RC Time Constant
It is usually useful to be able to control and predict with accuracy how long it takes for a capacitor to charge and discharge
This is accomplished by placing an appropriately sized resistor in series with the capacitor, thereby limiting the current and lengthening the time for the voltage to increase to source voltage
While the capacitor is being charged, the voltage between its terminals is an exponential function of time

## Slide 75: Electrical Fundamentals
Capacitance and Capacitors
RC Time Constant

## Slide 76: Electrical Fundamentals
Capacitance and Capacitors
RC Time Constant
Because t = RC, the formula can be rewritten as:
V(RC) = E (1 – e-1) = 0.632 E -- (0.632 is 63.2%)
The product of RC is called the RC time constant and is the time in seconds (t) required to charge the capacitor to 63.2% of the applied voltage (one time constant)
The capacitor is considered fully charged after five time constants (t = 5t) – charged to 99.3%

## Slide 77: Electrical Fundamentals
Capacitance and Capacitors
RC Time Constant
Amount of charge per time constant:
(t = 1t) = 63.2%
(t = 2t) = 86.5%
(t = 3t) = 95.0%
(t = 4t) = 98.2%
(t = 5t) = 99.3%*
*At (t = 5t), voltage reaches maximum value, so the circuit is considered fully charged

## Slide 78: Electrical Fundamentals
Capacitance and Capacitors
RC Time Constant
Discharging a capacitor using an RC time constant is essentially the same process in reverse
The capacitor is 63.2% discharged at (t = 1t); 86.5% at (t = 2t), etc., until it reaches (t = 5t), at which point it is 99.3% discharged*
*At (t = 5t), voltage drops to an immeasurably small value, so the circuit is considered fully discharged

## Slide 79: Electrical Fundamentals
Inductance and Inductors
Magnetic Fields & Magnetic Energy
Magnets are surrounded by magnetic fields in the same way that electric charges are surrounded by electric fields
Magnetic fields are represented by lines of force called magnetic flux representing a magnetic field, which is static and unchanging
All magnets have north and south poles
All magnetic lines of force form a loop through the north and south poles

## Slide 80: Electrical Fundamentals
Inductance and Inductors
Magnetic Fields & Magnetic Energy
Magnetic fields exist around two types of material
  Permanent magnets – Materials with high retentivity
  Electromagnets – Materials that rapidly lose their magnetic properties
Magnetic flux is measured in webers (Wb) in non-metric systems. One weber = one volt-second (1 Wb = 1 V-s). In metric systems, it is measured in maxwells (Mx). One maxwell = 10-8 weber (1 Mx = 10-8 Wb)
Magnetic field intensity (strength) is known as flux density (B), which is represented in gauss (G). One gauss = 1 maxwell per square centimeter measured perpendicularly to the direction of the magnetic field (1 G = Mx/cm2)

## Slide 81: Electrical Fundamentals
Inductance and Inductors
Magnetic Fields & Magnetic Energy
Magnetic flux or the magnetic field is produced by magnetomotive force (J) measured in gilberts (Gb)
The non-metric unit of magnetomotive force is the ampere-turn (A). (1 Gb = 0.79577 ampere-turn)
Magnetic field intensity (strength) is known as flux density (B), which is represented in gauss (G). One gauss = 1 maxwell per square centimeter measured perpendicularly to the direction of the magnetic field (1 G = Mx / cm2)

## Slide 82: Electrical Fundamentals
Inductance and Inductors
Magnetic Fields & Magnetic Energy
Magnetomotive force (J) is calculated by the following formula:

## Slide 83: Electrical Fundamentals
Inductance and Inductors
Magnetic Fields & Magnetic Energy
Magnetic field strength (H), measured in oersteds (Oe), is calculated by the following formula:

## Slide 84: Electrical Fundamentals
Inductance and Inductors
Magnetic Core Properties
Permeability (u) – The ratio of flux density produced by a given material compared to the flux density produced by an air core
Permeability (u) roughly corresponds to electrical conductivity.
Greater permeability (u) means that it is easier to establish a magnetic field
Less permeability (u) means that it is more difficult to establish a magnetic field

## Slide 85: Electrical Fundamentals
Inductance and Inductors
Magnetic Core Properties
Permeability is calculated using the following formula:
u = B / H
where
B is flux density in gauss (G)
H is the magnetic field strength in oersteds (Oe)

## Slide 86: Electrical Fundamentals
Inductance and Inductors
Magnetic Core Properties
Reluctance (R) – The reciprocal of permeability
Reluctance (R) roughly corresponds to resistance in an electrical circuit.
Greater reluctance (R) means that it is more difficult to establish a magnetic field
Less reluctance (R) means that it is less difficult to establish a magnetic field

## Slide 87: Electrical Fundamentals
Inductance and Inductors
Magnetic Core Properties
Reluctance (R) is calculated using the following formula:
R = J / B
where
J is magnetomotive force in gilberts (Gb)
B is flux density in gauss (G)

## Slide 88: Electrical Fundamentals
Inductance and Inductors
Magnetic Core Properties
Hysteresis – The condition of a magnetic material that causes it to retain a residual flux when all magnetizing force has been removed
Hysteresis represents a loss much like resistance in an electrical circuit
The residual flux can be removed by applying a coercive force
*Air cores are immune to hysteresis effects and losses

## Slide 89: Electrical Fundamentals
Inductance and Inductors
Magnetic Core Properties
  Saturation – The condition where an increase in current in an electromagnet results in no appreciable change in flux because all the magnetic material’s atoms are aligned
  Effects of saturation
    As long as the magnet’s coil current remains below saturation, the coil’s inductance remains constant
    Beyond the saturation point, inductance drops off

## Slide 90: Electrical Fundamentals
Inductance and Inductors
Magnetic Core Properties
The effect of saturation is depicted in the images. As current increases toward saturation, inductance remains constant (line A). When saturation is reached, inductance rolls off
As mentioned in the text, a small air gap is cut into the core, forcing the flux lines to travel through air for a short distance. The effect is depicted at line B

## Slide 91: Electrical Fundamentals
Inductance and Inductors
Inductance and Direct Current
  Inductor – Any device whose operation is based on transferring energy into and out of magnetic fields
  Inductors are often referred to as coils due to their construction
  Induced Voltage (Back Voltage) – The basic operating principle of the inductor whereby it resists current flow until the field become constant thus preventing current from rising too rapidly

## Slide 92: Electrical Fundamentals
Inductance and Inductors
Inductance and Direct Current
  The amplitude of the induced voltage is proportional to the rate at which the current and magnetic field changes, and to a constant associated with the inductor, referred to as inductance (L)
  The basic unit of inductance is the henry (H)

## Slide 93: Electrical Fundamentals
Inductance and Inductors
Inductance and Direct Current
  The amplitude of the induced voltage is calculated using the following formula:

## Slide 94: Electrical Fundamentals
Inductance and Inductors
Inductance and Direct Current
  An inductance of 1 H generates an induced voltage of 1 V when the inducing current is varying at a rate of 1 A/sec
  The (-) sign in the mathematical result indicates that the induced voltage is the opposite polarity of the applied current

## Slide 95: Electrical Fundamentals
Inductance and Inductors
Inductance and Direct Current
  The energy stored in the magnetic field of an inductor is calculated using the following formula, which corresponds to the energy storage formula for capacitors:

## Slide 96: Electrical Fundamentals
Inductance and Inductors
Inductor Notes
  The magnetic field strength (H) of an inductor is proportional to the number of turns in the inductor’s winding (N) and the permeability (u) of its core making it proportional to both (N) and (u)
  The polarity of the induced voltage is always such that it will oppose changes in circuit current – If current increases, opposition increases by storing energy; if current decreases, the stored energy is returned to the circuit
  The effect of this opposition is similar to that of a capacitor, which opposes changes in voltage

## Slide 97: Electrical Fundamentals
Inductance and Inductors
Mutual Inductance
  Mutual Inductance (Coupling) – The effect of inducing a voltage (and thus a current) on an inductor – or even a single wire conductor – by the charging of another inductor
  Coupling between inductors can be minimized by using separate closed magnetic cores for each inductor
  Unwanted Coupling – Coupling induced on another inductor or conductor that is not designed into the circuit, especially in fields changing at frequencies of 100 MHz or higher
    Computer bus lines and solder traces must be separated
    Shielding is often used when physical separation is not possible

## Slide 98: Electrical Fundamentals
Inductance and Inductors
Inductors in Series
  Inductor is series are treated similarly to resistors in series assuming no coupling
  The total inductance will be the sum of the individual inductors
    LTotal = L1 + L2 + L3 + …
    Example: LTotal = 5.0 mH + 20.0 mH + 8.0 mH = 33 mH

## Slide 99: Electrical Fundamentals
Inductance and Inductors
Inductors in Parallel
Inductors in parallel are treated similarly to resistors in parallel when calculating circuit values
The formula for finding inductors in parallel, sometimes referred to as the Reciprocal of Reciprocals formula:

## Slide 100: Electrical Fundamentals
Basic Circuit Principles
Inductors in Parallel
Example: Given three inductors (5.0 mH, 20.0 mH, 8.0 mH) the circuit has an inductance of:
Ltotal = 1 / (1/5.0 mH) + (1/20.0 mH) + (1/8.0 mH)
= 1 / 0.20 + 0.05 + 0.125
= 1 / 0.375
= 2.67 mH

## Slide 101: Electrical Fundamentals
Inductance and Inductors
Inductors in Parallel
If only two inductors in parallel, then the following formula can be used. (This can also be used to combine parallel inductors two at a time to keep from having to do the Reciprocal of Reciprocals formula)

## Slide 102: Electrical Fundamentals
Inductance and Inductors
RL Time Constant
As with a capacitor, it is usually useful to be able to control and predict with accuracy how long it takes for an inductor to build up and deplete full current
This is accomplished by placing an appropriately sized resistor in series with the inductor, thereby limiting the current and lengthening the time for the current to increase to source current

## Slide 103: Electrical Fundamentals
Inductance and Inductors
RL Time Constant

## Slide 104: Electrical Fundamentals
Inductance and Inductors
RL Time Constant
Because t = L/R, the formula can be rewritten as:
V(L/R) = E/R (1 – e-1) = 0.632 E/R -- (0.632 is 63.2%)
The RL time constant is the time in seconds (t) required to charge the inductor to 63.2% of the applied voltage (one time constant)
Current is considered to have reached maximum value after five time constants (t = 5t) – 99.3%

## Slide 105: Electrical Fundamentals
Inductance and Inductors
RL Time Constant
Amount of charge per time constant:
(t = 1L/R) = 63.2%
(t = 2L/R) = 86.5%
(t = 3L/R) = 95.0%
(t = 4L/R) = 98.2%
(t = 5L/R) = 99.3%*
*At (t = 5L/R), current increases to maximum value

## Slide 106: Electrical Fundamentals
Inductance and Inductors
RL Time Constant
Depleting an inductor’s current using an RL time constant is essentially the same process in reverse
The inductor is 63.2% discharged at (t = 1L/R); 86.5% at (t = 2L/R), etc., until it reaches (t = 5L/R), at which point it is 99.3% depleted*
*At (t = 5t), current drops to an immeasurably small value

## Slide 107: Electrical Fundamentals
  End of Presentation – Thank you!

## Slide 108
Questions?
You may email questions later to kq1s@arrl.net