## Slide 1
Welcome to the Antenna Summit

## Slide 2
Session 4 – Analog Integrated Circuits and Components

## Slide 3: Analog Integrated Circuits and Components Introduction
Instructor : Bill Smith, KQ1S
  Amateur Extra
  Licensed since 1983
The ARRL Handbook for Radio Communications, 98th Edition, 2021
  Sections 4.5.7 – 4.11.11

## Slide 4: Analog Integrated Circuits and Components Course Overview
        Transistors
        Op Amps
        Miscellaneous Analog ICs
        Timers
        Analog-Digital Interfacing
        Heat Management

## Slide 5: Analog Integrated Circuits and Components
Analog Amplifiers
  The most common type of analog circuit in use
  Amplification occurs when a small input signal controls a larger output signal
  The basic component of an amplifier is a Transistor
  Many designs today employ Integrated Circuit (IC) amplifiers
  One of the most common IC amplifiers is the Operational Amplifier (OP Amp)

## Slide 6: Analog Integrated Circuits and Components
Amplifier Terminology
  Input Impedance – The equivalent ac impedance that one observes looking into the input of a circuit or device
  Output Impedance – The equivalent ac impedance that one observes looking into the output of a circuit or device
  Gain (Voltage, Current, Power) – The ratio of output voltage, current, or power to input voltage, current, or power – V,C,POut/V,C,PIn = Gain
  Buffer – An amplifier used to provide isolation between two circuits
  Isolation – Lack of effect of one circuit from changes in another circuit

## Slide 7: Analog Integrated Circuits and Components
Semiconductor Amplifier Models
  Model – Semiconductor equivalent circuit design comprised of voltage and current sources, resistors, capacitors, and inductors
  Various models for specific purposes:
    Small-signal Model – Used when voltage and current interact in a near linear fashion
    Large-signal Model – Used when the device will be operated at saturation or cut-off
    Low-frequency Model – Used in DC, audio, and very low RF frequency applications
    High-frequency Model – Used for high frequency, high gain, or phase shift applications

## Slide 8: Analog Integrated Circuits and Components
Transistor Amplifiers - Bipolar Junction Transistor (BJT)

## Slide 9: Analog Integrated Circuits and Components
Bipolar Junction Transistor (BJT)
  Two Types – NPN and PNP
    NPN – N-type substrate with P-type channel infused
    PNP – P-type substrate with N-type channel infused

## Slide 10: Analog Integrated Circuits and Components
Bipolar Junction Transistor (BJT)
(Current flow is generally in the direction of the emitter arrow)

## Slide 11: Analog Integrated Circuits and Components
Bipolar Junction Transistor (BJT) Amplifiers
  Three Common BJT Amplifier Configurations
    Common-Emitter (Most common amplifier configuration)
    Common-Collector (Often referred to as an Emitter Follower)
    Common-Base
  BJT amplifiers are mainly current-controlled devices
  “Common” = The part of the transistor used by both the input and output

## Slide 12: Analog Integrated Circuits and Components
Common-Emitter Amplifier
  Most common small-signal amplifier
  Used when a modest voltage gain and a low to medium input impedance is required
  A positive increase in input amplitude increases base current and reduces collector current
  The output signal is inverted relative to its input signal

## Slide 13: Analog Integrated Circuits and Components
Common-Collector (Emitter-Follower) Amplifier
  Generally referred to as an Emitter-Follower amplifier
    Emitter voltage follows input voltage
    Exhibits unity voltage gain
  Used as a buffer amplifier to couple low impedance loads or protect sensitive circuits
  Used when a high input/low output impedance is required

## Slide 14: Analog Integrated Circuits and Components
Common-Base Amplifier
  Exhibits unity current gain
  Used when a low input/high output impedance is required
  Useful for Ham radio pre-amplifiers
  A positive increase in input amplitude reduces base current – VBE is lowered; VC is raised

## Slide 15: Analog Integrated Circuits and Components
Bipolar Junction Transistor (BJT) Comparison
NPN-Type | PNP-Type
If the base is at a lower voltage than emitter, current flows emitter-collector | If the base is at a higher voltage than the emitter, current flows collector-emitter
A small amount of current also flows emitter to base | A small amount of current also flows base to emitter
Emitter and collector not interchangeable | Emitter and collector not interchangeable
Voltage at base controls amount of current flow thru transistor (E-to-C) | Voltage at base controls amount of current flow thru transistor (C-to-E)
Current flows in direction of the arrow | Current flows in direction of the arrow

## Slide 16: Analog Integrated Circuits and Components
Analog Amplifier Operating Classes
Class | Characteristic
A | 100% duty cycle
B | 50% duty cycle
C | <50% duty cycle
AB | 50% to 100% duty cycle
AB-1, AB-2 | 50% to 100% duty cycle

## Slide 17: Analog Integrated Circuits and Components
Transistor Amplifiers – Field-Effect Transistor (FET)
    Widely used in radio and other RF applications today
      JFET – Junction Field Effect Transistor
      MOSFET - Metal-oxide-semiconductor Field Effect Transistor

## Slide 18: Analog Integrated Circuits and Components
Field-Effect Transistor (FET)

## Slide 19: Analog Integrated Circuits and Components
Field-Effect Transistor (FET)
  Two Types – N-channel and P-channel
    N-channel – N-type substrate with P-type channel infused
    P-channel – P-type substrate with N-type channel infused

## Slide 20: Analog Integrated Circuits and Components
Field-Effect Transistor (FET)

## Slide 21: Analog Integrated Circuits and Components
Field-Effect Transistor (FET)

## Slide 22: Analog Integrated Circuits and Components
Field-Effect Transistor (FET) Amplifiers
  Three Common FET Amplifier Configurations
    Common-Source (Corresponds to the common-emitter)
    Common-Drain (Referred to as a Source-Follower; Corresponds to the emitter-follower)
    Common-Gate (Corresponds to the common-base)
  FET amplifiers are strictly voltage-controlled devices
  “Common” = The part of the transistor used by both the input and output

## Slide 23: Analog Integrated Circuits and Components
Common-Source Amplifier
  Can be used as a variable resistance – Usually operates in saturation region
  The Drain-Source channel can be treated as a current source
  A positive increase in input amplitude reduces output voltage
  The output signal is inverted relative to its input signal (similar to CE)

## Slide 24: Analog Integrated Circuits and Components
Common-Drain (Source-Follower) Amplifier
  Generally referred to as a Source-Follower amplifier
    Source voltage follows input voltage
    Exhibits unity voltage gain
  Used as a buffer amplifier to couple low impedance loads or protect sensitive circuits
  Used when a high input/low output impedance is required

## Slide 25: Analog Integrated Circuits and Components
Common-Gate Amplifier
  Exhibits unity current gain
  Exhibits high voltage gain
  Used when a low input/high output impedance is required
  Useful for Ham radio pre-amplifiers
  Often chosen as pre-amplifiers because their high voltage gain and low input impedance can match coaxial cable impedances

## Slide 26: Analog Integrated Circuits and Components
Self-biased FET Amplifiers
  FET amplifiers are usually self-biased to prevent DC voltage build up affecting conductivity (CIN plus RG or RS)
Common-Source
Common-Drain
Common-Gate

## Slide 27: Analog Integrated Circuits and Components
Field-Effect Transistor (FET) Comparison
JFET | MOSFET
Comparatively harder to fabricate | Comparatively easier to fabricate
Operated only in depletion mode | Can be operated in both depletion and enhancement modes
Drain resistance is 1 MΩ – Results in flatter output characteristics | Drain resistance is 50 kΩ
Gate leakage current is roughly 10-9 Amp | Gate leakage current is roughly 10-12 Amp
Input resistance is roughly 108 Ω | Input resistance is in the range of 1010 Ω to 1015 Ω
Non-symmetrical device | Symmetrical device – Source and Drain terminals can be interchanged

## Slide 28: Analog Integrated Circuits and Components
Field-Effect Transistor (FET) Amplifiers
  Because of their advantages, MOSFETs are more widely used than JFETs
  MOSFETs are widely used in analog signal switching applications
  MOSFETs are highly susceptible to overload voltages – Care must be taken during handling and installation not to damage with static charges

## Slide 29: Analog Integrated Circuits and Components
Operational Amplifiers (Op Amps)
  One of the most widely used linear IC devices
  Built as a package to ensure close matching of circuit components
  Much higher performance than similar circuits built using discrete components
    Infinite input impedance
    Zero output impedance
    Open loop voltage gain near infinity

## Slide 30: Analog Integrated Circuits and Components
Operational Amplifiers (Op Amps)
- Though the Op Amp is valued for its nearly infinite input impedance, current in the nanoAmp range does actually flow
- At times, a small (mV) DC offset voltage, known as an input offset voltage, is applied to the input terminals through a potentiometer (The 741 Op Amp has pins for this purpose)

## Slide 31: Analog Integrated Circuits and Components
Operational Amplifiers (Op Amps)

## Slide 32: Analog Integrated Circuits and Components`
Operational Amplifiers (Op Amps)

## Slide 33: Analog Integrated Circuits and Components
Operational Amplifiers (Op Amps)
    Like transistors, Op Amps have a limited frequency response
    The upper bandwidth limit is called its Gain-Bandwidth Product (GBW)
      GBW is the maximum product of gain & frequency available in the circuit
      Voltage Gain x Frequency = GBW
      Example: Calculate the maximum frequency for an Op Amp with a GBW of 10 MHz connected to a x40 voltage amplifier = GBW/gain = 10 MHZ/40 = 250 kHz

## Slide 34: Analog Integrated Circuits and Components
Operational Amplifiers (Op Amps)
    Common Mode Signals (CMRR) – Signals (many times noise) that appear equally at all terminals
      Op Amps only respond to differences in voltage at the input terminals
      CMRR signals appear as equal voltages, so are rejected
      Very important for small signal circuits where noise could overpower desired signal
    Power Supply Rejection Ratio (PSRR) – The measure of an Op Amp’s ability to continue performing well despite power supply imbalance or noise
      Changes in power supply voltages translate to the Op Amp’s internal circuitry
      The ability to ignore these anomalies is highly desired

## Slide 35: Analog Integrated Circuits and Components
Operational Amplifiers (Op Amps)
    Rails – The voltage signal limits that an Op Amp can accept and amplify
      The theoretical limits are the upper and lower power supply voltages
      The voltages can be symmetrical or non-symmetrical, similar or dissimilar polarities
      In practice, Op Amps will clip the signal roughly 0.7 V to 1.4 V prior to the rail
      More precise rail-to-rail Op Amps have been developed to limit the clipping level to within
      tens of mV of the rails

## Slide 36: Analog Integrated Circuits and Components
Operational Amplifiers (Op Amps)
- In this circuit, the rails are +5 V and Ground
- The circuit clips the signals 4.4 V and 0.6 V
- (The 300 mV figure is referred to as headroom)

## Slide 37: Analog Integrated Circuits and Components
Op Amp Characteristics
Non-inverting – Input and output voltage polarity remain the same
Inverting – Input and output voltage polarity have an inverse relationship
Compensation – Used in older Op Amps to prevent oscillation at very high frequencies, capacitor placed across pins

## Slide 38: Analog Integrated Circuits and Components
Operational Amplifiers (Op Amps)
Non-inverting Amplifier
Inverting Amplifier
Summing Junction (Non-inverting Amp) – Connection point for Ri and Rf and the inverting (-) terminal
Summing Junction (Inverting Amp) – Connection point for Ri and Rf and the non-inverting (+) terminal
Loop Error Signal – Difference in voltage between the inverting and non-inverting terminals
Negative Feedback (Both Amps) – Return signal from the output opposing the input to stabilize the amp and prevent runaway

## Slide 39: Analog Integrated Circuits and Components
Operational Amplifiers (Op Amps)
*With the non-inverting Op Amp, we calculate the summing junction voltage VINV = VO (Ri / Ri + Rf) at time zero, when signal is first applied
*Eventually, the loop error signal will equal 0 V; that is, the voltage at (-) is equal to Vin, so VINV = Vin
*Given this situation, Gain is calculated as VO / Vin = ((1 + (Rf / Ri))
*Gain for the non-inverting Op Amp can vary from 1 to the Op Amp’s maximum
-------------------------------------------------------------------------------------------------------------
*With the inverting Op Amp, (+) is connected to circuit reference (ground)
*The current through Ri is balanced by an equal but opposite current through Rf
*Gain is calculated as VO / Vin = -(Rf / Ri) The output signal in inverted, hence the (-)
*Gain for the inverting Op Amp can vary from 0 to the Op Amp’s maximum (0-1 attenuate; 1 and above amplify)

## Slide 40: Analog Integrated Circuits and Components
Various Uses for Op Amps
      Unity-Gain Buffer (Voltage Follower) Amp
      Differential and Difference Amps
      Instrumentation Amp
      Comparator
      Active Filters

## Slide 41: Analog Integrated Circuits and Components
Unity-Gain Buffer (Voltage Follower) Amp
The Unity-Gain Buffer (voltage follower) is a special use of the Op Amp
Used as a buffer stage – Maximum input impedance, minimum output impedance
Output and input voltages are equal – Can be thought of as a repeater within the circuit
Used in both RF and telephony circuits

## Slide 42: Analog Integrated Circuits and Components
Differential and Difference Amps
The Differential Amp is also a special use of the Op Amp
Amplifies the difference between two analog signals
Primarily used for cancelling noise within the limits of CMRR
The calculation for differential amp operation is:

## Slide 43: Analog Integrated Circuits and Components
Differential and Difference Amps
The Difference Amp is a Differential Amp with all four resistor values being equal
Amplifies the difference between two analog signals
Primarily used for cancelling noise within the limits of CMRR
The calculation for Difference Amp operation is much simpler because VO is just the difference of the two stages:
VO = Vn – VI

## Slide 44: Analog Integrated Circuits and Components
Instrumentation Amp
The Instrumentation Amp is a special purpose Op Amp used to further improve the impedance, gain, and CMRR characteristics of single Op Amps
Usually manufactured in one IC to match internal device and temperature characteristics
Usually employ carefully matched external resistors, many times an integrated resistor pack
The design is of the inputs connected to two non-inverting Buffer Amps (with Gain = 1 + R2/R1), with their outputs connected to a Differential Amp (with Gain = R4/R3)
Result: A higher performing amp (impedance, gain, and CMRR) than any single Op Amp over a wider temperature range

## Slide 45: Analog Integrated Circuits and Components
Summing Amps
The Summing Amp is a special purpose Op Amp that takes advantage of the Op Amp’s high input impedance
Multiple input signals are connected together (summed) through resistors at the Op Amp’s input
A few Amateur Radio summing applications:
https://kb8fir.wordpress.com/2014/07/16/using-a-small-audio-mixer-for-ham-shack/
https://n0eck.wordpress.com/2013/09/05/connecting-a-mixer-to-your-ham-radios/
https://w3yy.com/audio_control_system.htm

## Slide 46: Analog Integrated Circuits and Components
Summing Amps – Determining Output
The output of the inverting Summing Amp is the sum of each input signal multiplied by its gain
Recall that VO/Vin = (1 + Rf / Ri)
Summing Amp output = (Vi1 + Vi2 + … Vim) x (1 + Rf / Ri)

## Slide 47: Analog Integrated Circuits and Components
Summing Amps – Determining Output
The output of the non-inverting Summing Amp is the gain times the weighted sum of the total (m) different input signals
Where Rpm = the parallel resistance of all m resistors excluding Rm – Example: Three input signals, Rp1 = the parallel combination of R2 and R3

## Slide 48: Analog Integrated Circuits and Components
Comparators
A Comparator is another specialty Op Amp that compares input voltages and determines TRUE or FALSE status depending on which input is higher
If non-inverting input is higher, the result is given as TRUE
If inverting input is higher, the result is given as FALSE
TRUE usually means a positive output voltage; FALSE usually means a negative or zero output voltage
A Setpoint voltage can be established to compare unknown signals against – indicates if unknown voltage is above or below the setpoint

## Slide 49: Analog Integrated Circuits and Components
Comparators
Chatter – Comparator output switching rapidly back and forth when the input is close to the setpoint
Hysteresis – A form of positive feedback that electrically moves the setpoint by a small amount (mV) in the direction opposite to that in which the input signal crossed the setpoint
Comparator Uses – Detect connection of accessories, Repeater voting, Peak detector, CI-V band detection by Icom

## Slide 50: Analog Integrated Circuits and Components
Active Filters – Low Pass Filters
Source: http://www.physics.unlv.edu/~bill/PHYS483/op_amp_filt.pdf

## Slide 51: Analog Integrated Circuits and Components
Active Filters – High Pass Filters
Source: http://www.physics.unlv.edu/~bill/PHYS483/op_amp_filt.pdf

## Slide 52: Analog Integrated Circuits and Components
Active Filters – Band Pass Filters
Source: http://www.physics.unlv.edu/~bill/PHYS483/op_amp_filt.pdf

## Slide 53: Analog Integrated Circuits and Components
Rectifier
Half-wave Precision Rectifier
Full-wave Precision Rectifier
Using an Op Amp Rectifier instead of a simple diode rectifier is that the Op Amp overcomes the voltage drop loss (0.7 V) across the diode alone

## Slide 54: Analog Integrated Circuits and Components
Peak Detector
The output capacitor (C) is charged when the Op Amp output goes positive
The capacitor is held charged by the blocking of the diode (current cannot flow backward through it)
The resistor (R) sets the capacitor time constant to determine its rate of discharge
A transistor in place of (R) could be used as a reset switch

## Slide 55: Analog Integrated Circuits and Components
Log Amplifier
Called a Log Amplifier because its large signal gain is proportional to the logarithm of the input signal’s amplitude AV = ln(Vin)
Small signal inputs (those too small to cause current flow through the diodes) have a normal gain of a regular inverting amplifier AV = -Rf/Ri
Small signals have to increase less (than large signals) to balance input voltages
The larger the input voltage, the greater conduction through the diodes, lowering the gain of the circuit logarithmically

## Slide 56: Analog Integrated Circuits and Components
Voltage-Current Converters
Op Amps are used for Voltage-Current Converters due to their impedance characteristics
The Op Amp’s high input impedance insures very little chance of coupling between the input voltage source and the output current
Frequently used to convert currents from sensors and detectors (see photodiode example at left) into voltages that are easier to measure (e.g., smoke detectors)

## Slide 57: Analog Integrated Circuits and Components
Component Arrays
A huge advantage of integrated circuits is the ability to combine multiple components in one integrated package
These types of arrays can contain transistors, diodes, capacitors, resistors, storage, and even inductors
Known as Application Specific Integrated Circuits (ASIC)

## Slide 58: Analog Integrated Circuits and Components
Transistor & Driver Arrays
Features
• Output voltage to 50V
• Output current to 500mA
• Transient-protected outputs
• Integral clamp diodes
• TTL, CMOS, or PMOS compatible inputs
Applications
• Relay and solenoid switching
• Stepping motor
• LED and incandescent displays
(2V / 40mA)

## Slide 59: Analog Integrated Circuits and Components
Voltage Regulators
Voltage Regulator Controller – 500mA, 3.3V +/-2%
PWM 30A, 12V Solar Charge Controller/Voltage Regulator
Voltage Regulators/Controllers – Three lead ICs that contain all the circuit components to provide voltage regulation
Voltage can be fixed or variable
Variable Voltage Controller

## Slide 60: Analog Integrated Circuits and Components
Timers (Multivibrators)
  Multivibrator – A circuit that oscillates (vibrates) between two states, most often generating a square wave or pulse train output
          Monostable (One Shot) Multivibrator
          Astable Multivibrator
          Bistable (Flip-Flop) Multivibrator

## Slide 61: Analog Integrated Circuits and Components
555 Timer
By far, the most common timer (multivibrator) is the 555 timer (NE555 or LM555)
Is used as the basic circuit for monostable, astable, and bistable multivibrators
Operates within the frequency range of less than 1 Hz to several hundred kHz

## Slide 62: Analog Integrated Circuits and Components
555 Timer

## Slide 63: Analog Integrated Circuits and Components
Timers (Multivibrators)
Once triggered, continues to change states at a predictable rate. Common uses: clock signals, timing signals, vehicle turn indicators, strobe lights, etc.
Once triggered, creates a perfect square wave (one), then returns to quiescent state until triggered again. Common uses: Pulse generator, circuit time delay, reduce pulse distortion in computer systems, etc.
Once triggered, remains in the high state until reset by a separate reset trigger. Common uses: Computer memory circuits, counting circuits, etc. Several different types of Bistable Multivibrators depending on the desired use

## Slide 64: Analog Integrated Circuits and Components
Analog - Digital Interfacing
24VAC Motor Output
120VAC Input

## Slide 65: Analog Integrated Circuits and Components
Analog - Digital Interfacing
Antenna Rotator Controller, KG4JJH
http://www.kg4jjh.com/pdf/antenna%20rotator%20controller.pdf
CMPS03 Compass Sensor Module
https://www.robot-electronics.co.uk/htm/cmps3tech.htm

## Slide 66: Analog Integrated Circuits and Components
Heat Management Principles
    Heat dissipation is extremely critical for safe and efficient operation of analog and digital circuits
    Integrated Circuits and high-power discrete components are particularly vulnerable to improper heat dissipation
    When considering heat dissipation, always calculate using Peak-to-Peak (not RMS) voltages of a circuit under full load (most devices list the average voltage on their packaging)
    Rule of Thumb: Choose devices with a maximum power dissipation of twice the desired output power
    Use “Thermal Grease” with heat sinks as specified by device manufacturer
    Device resistance will decrease 6% - 8% per Celsius degree until the device eventually offers too little resistance to current flow, and it fails
    RF current will often cause overheating where a similar level of DC current will not
    DUST IS YOUR ENEMY!!

## Slide 67
Thank you for your participation
Questions?
You may email questions to kq1s@arrl.net
This presentation is available at:
https://www.hamradioedu.com - Click on PRESENTATIONS