## Slide 1
Welcome to the Antenna Summit
Sponsored by NADXA
Northern Arizona DX Association

## Slide 2
Thank You
NAU – Cline Library

## Slide 3
Session 6 – ARRL Antenna Book
Chapter 1 - Antenna Fundamentals

## Slide 4: Instructor
Ron Gerlak
KG7OH – Amateur Extra Class
Licensed 1977
ARRL ANTENNA BOOK 24th Edition 2019
Q & A at the end of each chapter
Via Chat
Email questions to: KG7OH@arrl.net - Anytime

## Slide 5: Radio System
Radio Puzzle
Transmitter, Receiver and Antenna System
Get a Signal from Your Transmitter to
The other hams Antenna
Propose of Antennas
Radiate and receive electrometric waves
Reciprocity
Always & Never

## Slide 6: Dissipated Electromagnetic Waves
  Radiated as Heat 😩
  Antennas close to ground
  Antennas made of very small wire
  Reducing Losses = Increased Radiation Efficiency
Dissipated Electromagnetic Waves
  Radiation of Electrometric Waves 😀

## Slide 7: ANTENNAS
H = Magnetic Field
E = Electrical Field
Determines Polarization
Electromagnetic Waves

## Slide 8
Array of Light (Next Generation of Antennas)
Tom Schiller, N6BT
          ANTENNAS
Anything Works (Tom Schiller, N6BT)
Everything matters

## Slide 9: What Matters
Directivity
Gain
Take-Off Angle
Type of Ground
Height Above Ground
Near & Far Fields
Free Space
VSWR
Impedance

## Slide 10: Impedance
Feed Point Impediance
  Self and Mutual Impedance
  Feed Point Impedance is Low where the voltage is low
    At the center of a dipole
  Resonance
  An antenna can be resonant only at one frequency
  Current and voltage are in phase

## Slide 11: Fields
Near Field
Far Field
Boundary = D = 2L2/Wavelength
(Within 2 Wavelengths of the Feed Point)

## Slide 12: DIPOLE ANTENNA

## Slide 13: E and H Wave Forms

## Slide 14: Antenna Voltage and Current Distribution

## Slide 16: Decibels
Measures intensity of sound and power
So Double the power twice = 1 S-unit
+6dB = +1 S-unit Higher
Power x 2 = +3dB = 3dB Gain
Just add them up or subtract them
Log scale

## Slide 17: Power – dB – S Units
From 100 watts to 200 watts = + 3dB.
From 200 watts to 400 watts = +3dB.
3dB + 3dB = 6 dB = 1 S-unit
S 6

## Slide 18: Power – dB – S Units
From 100 watts to 200 watts = + 3dB.
From 200 watts to 400 watts = +3dB.
3dB + 3dB = 6 dB = 1 S-unit
S 7

## Slide 19: - or -
Change from a Dipole to a 3 element Yagi
= + 6 dBd = 1 S-unit
Same transmit result doubling + doubling power
Considerable improvement in receiving
S 6

## Slide 20: - or -
Change from a Dipole to a 3 element Yagi
= + 6 dBd = 1 S-unit
Same transmit result doubling + doubling power
1 S-unit improvement in receiving
S 7

## Slide 21: Fields and Waves
RF Waves change with time (Electromagnetic)
E Fields
Electric Wave
90 Degrees to the H Field
Increases with Voltage
Most Relevant to Ham Radio
Describes the Polarization of an Antenna
H Fields
Magnetic Wave
Increases with Current

## Slide 22: TYPES of PATTERNS
3D Pattern
Azimuthal Pattern
Elevation Pattern

## Slide 23: ISOTROPIC ANTENNA

## Slide 24: 3D ISOTROPIC ANTENNA PATTERN

## Slide 25: ISOTROPIC ANTENNA PATTERN SLICE
Elevation Pattern
Azimuthal Pattern

## Slide 26: Horizontal Dipole
The dipole is the simplest type of real antenna from a theoretical point of view. Most commonly it consists of two conductors of equal length oriented end-to-end with the feed-line connected between them.

## Slide 27: 3D DIPOLE ANTENNA PATTERN

## Slide 28: 3D DIPOLE PATTERN SLICE

## Slide 29: DIPOLE PATTERN
Horizontal Pattern
Azimuth Pattern
Vertical Pattern Elevation Pattern

## Slide 30: Horizontal Dipole Pattern
3D Pattern
Azimuth Pattern
Isotropic shown in Red

## Slide 31: Gain
  Dipole has 2.15 dBi gain over an Isotropic Antenna
  Signal from the ends is redistributed to the broadside

## Slide 32: Gain
Gain is achieved by redistribution of pattern
Where does the gain come from???
Antennas are passive devices and do not generate any “extra” power.

## Slide 33: DB Referance
Isotropic antenna as the reference
    Dipole has 2.15 dBi Gain
    Yagi has ≈ 6 dBd Gain
    Dipole antenna as the reference
    Yagi has ≈ 8.15 dBi Gain
    (Same antenna)
    Isotropic antenna as the reference

## Slide 34: Tri-Band Yagi 10 – 15 - 20

## Slide 35: YAGI (Gain Antenna) PATTERN (Azimuth)

## Slide 36: Azimuth ½ Power Points of a Yagi
0
90
180
270
30 Degrees
-3
-6
-9
0 dB
3 dB Down
½ Power Point
Beam Width

## Slide 37: Q - Quality
Narrower Beam width = Higher Q
Higher the Gain = Higher Q
More Selectivity
More Directivity
More Gain

## Slide 38: Q - Quality

## Slide 39: Q - Quality
Beam Width of Antennas
Transistors
Resonant RLC Circuits

## Slide 40: Azimuth ½ Power Points of a Yagi
0
90
180
270
20 Degrees
-3
-6
-9
0 dB
3 dB Down
½ Power Point
High “Q”
Beam Width

## Slide 41: Elevation Pattern of a Yagi
0
90
180
270
-3
-6
-9
0 dB

## Slide 42: Polarization
Horizontal
Vertical
Circular
Sky-waves

## Slide 43: Scaling
Scaling
Length, Spacing, Boom & Element Diameter

## Slide 44: ERP & EIRP (EiRP) Effective Radiated Power
TPO = 100 watts = 50 dBm
Transmission line attenuation = 2.4 dB
Losses in RF connectors and coupling = 1.7dB
Antenna gain = 7.5 dBi
EIRP = 50 dBm – 2.4 dB – 1.7 dB + 7.5 dB =
53.4 dBm = 219 watts

## Slide 45: Safety
Thermal Effects
Athermal Effects
Radiation
Power Density
Safe Levels
Pacemakers

## Slide 46: Thermal Effects of RF
Microwave cooks using RF Energy
Body’s Natural Resonant Frequency
  35 MHz – Grounded
  70 MHz - Insulated from ground
SAR – Specific Absorption Rate
MPE – Maximum Permissible Exposure

## Slide 47: Athermal Effects of EMR Electromagnetic Radiation Electromagnetic Field
Energy Fields – At Home/Work
  Electric Drill, 500 – 2000 milligauss
  Hair Dryer, 200 – 2000 milligauss
  Electric Blanket, 30 – 90 milligauss
  HF Transceiver , 10 – 100 milligauss
More studies – No association
Some studies – Weak association
  EMF & Malignant Conditions

## Slide 48: Radiation
Ionizing – Always a danger
  X Rays
  Gamma Rays
  Nuclear Power
Non-Ionizing – Sometimes a Concern
  RF Field
  60 Hz Field

## Slide 49: Power Density
Scientific community disagree on guidelines
Measurement equipment is expensive
ARRL RF Awareness Guidelines
  Page 1.24, Table 1.3

## Slide 50: ARRL RF Awareness Guidelines
Keep people away from antennas
Keep mobile power to < 25 watts
Make antenna heights > 35’
Keep equipment covers installed
Don’t point directional antennas toward people
Use a speaker microphones with HT radios
Keep a distance from transformers & fans

## Slide 51: Safe Exposure Levels STATIONS MUST BE EVALUATED
Controlled Environments
Uncontrolled Environments
E Field
H Field
Different Frequencies
Time Period Averaging
Experts Do Not Agree

## Slide 52: Safe Exposure Levels NO EVALUATIONS REQUIRED
100 maximum watts okay an all Bands except:
50 watts or less on:
12 Meters
10 Meters
VHF
UHF
(Table B, Page 1.21)

## Slide 53: Pacemakers
DISCUSS THIS WITH YOUR PHYSICIAN!

## Slide 54
Session 6 – ARRL Antenna Book
Chapter 2 - Dipoles and Monopoles

## Slide 55: Dipoles and Monopoles
Effects of Conductor Diameter
Radiation Patterns and Effects of Ground
Feed Point Impedance
Effects of Frequency on Radiation Pattern
Folded Dipoles
Vertical Dipoles
Off Center Fed (OCF) Dipoles
Monopoles
Folded Monopoles

## Slide 56: DIPOLES
Fundamental Antenna

## Slide 57: Dipole Length Calculations
λ/2 Dipole Resonant Length (in free space)
491.786 / f(in MHz) = Length in Feet
Example of 40 Meter Dipole:
491.786 / 7.2 = 68.29’

## Slide 58: Dipole - K Factor Length Correction for Diameter
Dipole Length Corrected for Diameter of #12 AWG
(.969 - .976) Page 2.2, Figure 2.3
491.786 / 7.2 = 68.29’
.97 x 491.786 / 7.2 = 66.3 Feet

## Slide 59: Dipole - Velocity Factor
Dipole Length Corrected for Insulated Wire
Reference Material says about .95%
My experience says about .99%
491.786 / 7.2 = 68.29’
.97 x 491.786 / 7.2 = 66.25’
.99 x .97 x 491.786 / 7.2 = 65.60’

## Slide 60: Dipole – Type of Ground
Very Poor Soil Ground
Good Ground
Salt Water

## Slide 61: Dipole – Height Factor
Resonant length changes up and down as the height above ground changes.

## Slide 62: Dipole Length USE THIS FORMULA IN THE FIELD
The book says 468 / f for λ/2
Soooo 234 / f(MHz) = the λ/4 element Length
Cut it 2 feet longer and wrap it back on itself.
Element length =
234 / f
then add 2’ just in case
234 / 7.2 = 32.5 Then add 2 = 34.5

## Slide 63: DIPOLES
Fundamental Antenna
Wrap extra wire here
Wrap extra wire here
Make these the actual calculated length

## Slide 64: Dipole Length
Check SWR dip with Antenna Analyzer
Adjust as needed:
Lengthen Antenna Lowers Dip Frequency

## Slide 65: Dipole Length
To lower the dip make the antenna longer

## Slide 66: Dipole Length
Needs to be more longer

## Slide 67: Dipole Length
Just the right length

## Slide 68: Dipoles Height Above Ground

## Slide 69: DIPOLES
Fundamental Antenna

## Slide 70: Folded Dipole

## Slide 71: Monopole / Vertical

## Slide 72: Vertical Dipole

## Slide 73: OCF Dipole

## Slide 74: Antenna Voltage and Current Distribution

## Slide 75: Feed Point Impedance
Dipole feed point impedance = 72 Ω
Vertical Monopole feed point impedance = 36 Ω
Inverted V feed point impedance = 50 Ω
Folded Dipole feed point impedance = 280 Ω
OCF Dipole feed point impedance = 150 - 300 Ω
Slopped feed point impedance = 80 Ω

## Slide 76: Antenna Modeling
EZNEC
www.eznec.com

## Slide 77
Next Session –
ARRL ANTENNA BOOK
Chapter 3
The Effects of Ground